## Slide 1: CL-716 Modelling Chemical and Biological Patterns BIFURCATION ANALYSIS OF NONLINEAR REACTION-DIFFUSION EQUATIONS
Project Presentation
Group 11
Date: 16th Apr 2015
Akash Deep Singhal (11D020024)
Amit Agarwal (11D020014)

## Slide 2: Abstract
The theoretical expressions are limited to the neighborhood of the marginal stability point. Computer simulations allow not only the verification of their predictions but also the investigation of the behavior of the system for larger deviations from the instability point.

## Slide 3: Introduction
Chemical Reaction
Rate Equation
Boundary Conditions

## Slide 4: Chemical Reaction
The theory of dissipative structures have been illustrated on a simple model system involving the following set of coupled chemical reactions:
The system is open to the initial and final chemicals A, B, D and E, whose concentrations are imposed throughout the system
Nonlinearity is introduced by the auto- and cross-catalytic steps (b) and (c);

## Slide 5: Rate Equations
The rate equations of our nonlinear reaction-diffusion system are given by:
Where, Dx and Dy are the diffusion coefficients of X and Y
Assumption: Fick’s law is valid

## Slide 6: Boundary Conditions
Two types of boundary conditions will be considered:
Zero flux boundary conditions (Neumann conditions):
Fixed boundary conditions (Dirichlet conditions):

## Slide 7: Matlab Code
The main script
PDE Solver
Initial Condition
Boundary Conditions

## Slide 8: Matlab Code
The main script file

## Slide 9: Matlab Code
PDE solver

## Slide 10: Matlab Code
Initial Conditions

## Slide 11: Matlab Code
Boundary Conditions

## Slide 12: Numerical Analysis
Simulation using Matlab
Space-time Plots

## Slide 13: Numerical Analysis
We use the simulation using MATLAB to verify the numerical results with the analytical ones.
Following are the major numerical simulations:-

## Slide 14: Numerical Analysis
Case 1
All the equations are restricted to the constraint 0 ≤ r ≤ L and L is taken to be 1.
Also diffusion coefficients are taken to be:-
  Dx = 1.6 x 10-3
  Dy = 8.0 x 10-3
A = 2 and B = 3.7 for zero flux boundary condition
Y vs distance ‘r’ and time ‘t’
X vs distance ‘r’ and time ‘t’

## Slide 15: Numerical Analysis
Case 2
All the equations are restricted to the constraint 0 ≤ r ≤ L and L is taken to be 1.
Also diffusion coefficients are taken to be:-
  Dx = 8.0 x 10-3
  Dy = 1.6 x 10-3
A = 2 and B = 3.7 for zero flux boundary condition
Y vs distance ‘r’ and time ‘t’
X vs distance ‘r’ and time ‘t’

## Slide 16: Analytical Solution
General solution
Linear Stability Diagrams
Comparison
Critical Wavenumber

## Slide 17: Analytical Solution
For zero – flux boundary conditions,
Inserting this into the rate equations, we get secular equation relating wn to the wavenumber n and the system's parameters:

## Slide 18: Analytical Solution
Instability of the thermodynamic branch will occur for some value of n, if at least one of the roots of (2.6) has a positive Re wn part. The main point is thus to establish the conditions for marginal stability, Re wn = 0, corresponding either to 'exchange of stability', Im wn = 0, or to 'overstability' Im wn ≠ 0. A close analysis of (2.6) shows that:

## Slide 19: Analytical Solution
For real wn’s the instability conditions reads:-

## Slide 20: Linear stability diagram
Case I
A=2
B=3.7
L=1
Dx = 8.0 x 10-3
Dy = 1.6 x 10-3
Chart: n
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
2.8 | 5 | 5.0948 | 5.3793 | 5.8534 | 6.5172 | 7.3706 | 8.4137 | 9.6464 | 11.0688 | 12.6808 | 14.4824 | 16.4738 | 18.6547 | 21.0253 | 23.5856 | 26.3355 | 29.2751 | 32.4043 | 35.7231 | 39.2316 | 42.9298 | 46.8176 | 50.8951 | 55.1622 | 59.6189 | 64.2653 | 69.1014 | 74.1271 | 79.3424 | 84.7474 | 90.342
2.13 | 274.1782 | 84.5909 | 49.8333 | 38.083 | 33.0995 | 30.8753 | 30.0373 | 30.012 | 30.5253 | 31.433 | 32.6532 | 34.1366 | 35.8521 | 37.7793 | 39.9045 | 42.2179 | 44.7127 | 47.3838 | 50.2275 | 53.2409 | 56.4219 | 59.7688 | 63.2802 | 66.9552 | 70.7927 | 74.7922 | 78.9531 | 83.2748 | 87.7571 | 92.3996

## Slide 21: Linear stability diagram
Case II
A=2
B=3.7
L=1
Dx = 1.6 x 10-3
Dy = 8.0 x 10-3
Chart: n
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
2.8 | 5 | 5.0948 | 5.3793 | 5.8534 | 6.5172 | 7.3706 | 8.4137 | 9.6464 | 11.0688 | 12.6808 | 14.4824 | 16.4738 | 18.6547 | 21.0253 | 23.5856 | 26.3355 | 29.2751 | 32.4043 | 35.7231 | 39.2316 | 42.9298 | 46.8176 | 50.8951 | 55.1622 | 59.6189 | 64.2653 | 69.1014 | 74.1271 | 79.3424 | 84.7474 | 90.342
2.13 | 52.4356 | 14.5182 | 7.5667 | 5.2166 | 4.2199 | 3.7751 | 3.6075 | 3.6024 | 3.7051 | 3.8866 | 4.1306 | 4.4273 | 4.7704 | 5.1559 | 5.5809 | 6.0436 | 6.5425 | 7.0768 | 7.6455 | 8.2482 | 8.8844 | 9.5538 | 10.256 | 10.991 | 11.7585 | 12.5584 | 13.3906 | 14.255 | 15.1514 | 16.0799

## Slide 22: Linear stability diagram: Comparison
Case I
Case II
Chart: n
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
2.8 | 5 | 5.0948 | 5.3793 | 5.8534 | 6.5172 | 7.3706 | 8.4137 | 9.6464 | 11.0688 | 12.6808 | 14.4824 | 16.4738 | 18.6547 | 21.0253 | 23.5856 | 26.3355 | 29.2751 | 32.4043 | 35.7231 | 39.2316 | 42.9298 | 46.8176 | 50.8951 | 55.1622 | 59.6189 | 64.2653 | 69.1014 | 74.1271 | 79.3424 | 84.7474 | 90.342
2.13 | 274.1782 | 84.5909 | 49.8333 | 38.083 | 33.0995 | 30.8753 | 30.0373 | 30.012 | 30.5253 | 31.433 | 32.6532 | 34.1366 | 35.8521 | 37.7793 | 39.9045 | 42.2179 | 44.7127 | 47.3838 | 50.2275 | 53.2409 | 56.4219 | 59.7688 | 63.2802 | 66.9552 | 70.7927 | 74.7922 | 78.9531 | 83.2748 | 87.7571 | 92.3996
Chart: n
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
2.8 | 5 | 5.0948 | 5.3793 | 5.8534 | 6.5172 | 7.3706 | 8.4137 | 9.6464 | 11.0688 | 12.6808 | 14.4824 | 16.4738 | 18.6547 | 21.0253 | 23.5856 | 26.3355 | 29.2751 | 32.4043 | 35.7231 | 39.2316 | 42.9298 | 46.8176 | 50.8951 | 55.1622 | 59.6189 | 64.2653 | 69.1014 | 74.1271 | 79.3424 | 84.7474 | 90.342
2.13 | 52.4356 | 14.5182 | 7.5667 | 5.2166 | 4.2199 | 3.7751 | 3.6075 | 3.6024 | 3.7051 | 3.8866 | 4.1306 | 4.4273 | 4.7704 | 5.1559 | 5.5809 | 6.0436 | 6.5425 | 7.0768 | 7.6455 | 8.2482 | 8.8844 | 9.5538 | 10.256 | 10.991 | 11.7585 | 12.5584 | 13.3906 | 14.255 | 15.1514 | 16.0799

## Slide 23: Linear stability diagram: Validity Verification (Case I)
Numerical
Analytical
Chart: n
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
2.8 | 5 | 5.0948 | 5.3793 | 5.8534 | 6.5172 | 7.3706 | 8.4137 | 9.6464 | 11.0688 | 12.6808 | 14.4824 | 16.4738 | 18.6547 | 21.0253 | 23.5856 | 26.3355 | 29.2751 | 32.4043 | 35.7231 | 39.2316 | 42.9298 | 46.8176 | 50.8951 | 55.1622 | 59.6189 | 64.2653 | 69.1014 | 74.1271 | 79.3424 | 84.7474 | 90.342
2.13 | 274.1782 | 84.5909 | 49.8333 | 38.083 | 33.0995 | 30.8753 | 30.0373 | 30.012 | 30.5253 | 31.433 | 32.6532 | 34.1366 | 35.8521 | 37.7793 | 39.9045 | 42.2179 | 44.7127 | 47.3838 | 50.2275 | 53.2409 | 56.4219 | 59.7688 | 63.2802 | 66.9552 | 70.7927 | 74.7922 | 78.9531 | 83.2748 | 87.7571 | 92.3996

## Slide 24: Linear stability diagram: Validity Verification (Case II)
Numerical
Analytical
Chart: n
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
2.8 | 5 | 5.0948 | 5.3793 | 5.8534 | 6.5172 | 7.3706 | 8.4137 | 9.6464 | 11.0688 | 12.6808 | 14.4824 | 16.4738 | 18.6547 | 21.0253 | 23.5856 | 26.3355 | 29.2751 | 32.4043 | 35.7231 | 39.2316 | 42.9298 | 46.8176 | 50.8951 | 55.1622 | 59.6189 | 64.2653 | 69.1014 | 74.1271 | 79.3424 | 84.7474 | 90.342
2.13 | 52.4356 | 14.5182 | 7.5667 | 5.2166 | 4.2199 | 3.7751 | 3.6075 | 3.6024 | 3.7051 | 3.8866 | 4.1306 | 4.4273 | 4.7704 | 5.1559 | 5.5809 | 6.0436 | 6.5425 | 7.0768 | 7.6455 | 8.2482 | 8.8844 | 9.5538 | 10.256 | 10.991 | 11.7585 | 12.5584 | 13.3906 | 14.255 | 15.1514 | 16.0799

## Slide 25: Critical Wave Number
The critical wave number corresponding to the onset of stability is given by nmin if it is an integer or by one of the two closest integers.
Case I: A=2, B=3.7, L=1, Dx = 8.0 x 10-3, Dy = 1.6 x 10-3
Critical Wave number = [1/∏ * 21/2/(8*10-3*1.6*10-3)1/4 ] = 8
Case II: A=2, B=3.7, L=1, Dx = 1.6 x 10-3, Dy = 8.0 x 10-3
Critical Wave number = [1/∏ * 21/2/(1.6*10-3*8*10-3)1/4 ] = 8 (same)

## Slide 26: Extended Analysis
Analytical steady state dissipative structure
Properties of the Dissipative Structure
Matlab code

## Slide 27: Analytical steady state dissipative structure
We have,
The bifurcating non uniform steady state solution near B = Bc is thus approximated by:

## Slide 28: Matlab Code

## Slide 29: Dissipative structure pattern
X v/s r
Y v/s r
Results obtained from the simulation of the above MATLAB code; Matched with the original solution given in figure 5a and 5b in the paper.

## Slide 30: Pattern from numerical integration of steady state rate equation
And the pattern obtained from numerical integration of equation 1.2,
comes out to be as follows:-

## Slide 31: References
J. F. G. Auchmuty and Nicholis G. Bifurcation analysis of Nonlinear Reaction-Diffusion Equations - I [Journal]. - [s.l.] : Bull. Math. Biology, 1974. - Vol. 37.
Kaufman M. Herschkowitz Bifurcation analysis of non-linear reaction-diffusion equations - II [Journal]. - Belgium : [s.n.], 1975. - Vol. 37.
Murray J. D. Mathematical Biology [Book]. - Vol. II.
Solving Initial-Boundary value problems for parabolic-elliptic PDEs in 1-D [Online] // Mathworks India. - http://in.mathworks.com/help/matlab/ref/pdepe.html.

## Slide 32: Thank You